## Slide 1: Introduction to Stage Lights
Module 2 – Lenses, Lamps, Reflectors, and Instruments

## Slide 2: Lenses
Lenses are used to bend light
  Depending on the shape of the lens, we can spread or compress the light rays
Sometimes it takes more than one lens to achieve correct shape
  The use of multiple lenses in combination are called a lens train

## Slide 3: Light in air versus in glass
Light traveling through air will not be disrupted
  The angle from the source of light does not change
When glass is placed in between, the light rays are altered
  Within the glass, an exaggerated angle of bend takes place
  The specific amount bend is how instrument manufactures control beam angles

## Slide 4: Lens types
Plano-convex lens
  A “D” shape, with one flat side and convex side
Bi-convex lens
  A lens with both convex sides, appears to be bulging “( )”
Convex-concave lens
  Has one convex and one concave side
Fresnel lens
  A modified plano-convex lens redesigned to reduce
  lens thickness

## Slide 5: What is a conventional?
A conventional fixture is one that uses a Tungsten-halogen lamp
  These have been around for a long time
  Known to get hot

## Slide 6
Incandescent
lamp

## Slide 7
Tungsten-halogen
lamp

## Slide 8: Lamp life
The lamp life is NOT when the amount of time until the lamp burns out, but the amount of time until the light being emitted is only 60%
Most conventional lamps have a lifespan < 2,000 hours
Right before a lamp blows, it often will appear brighter,
why do you think that is?

## Slide 9: Arc source lamps
Light generated is from a electrical arc jumping between 2 electrodes
  In the same way that light is emitted from a welder
Regularly very blue-white in color
Frequently found in projectors
NOT Dimmable
  Needs a physical shutter or dowser
Often have a warm-up period and can’t be immediately turned back on

## Slide 10: Color temperature
In terms of white light, we can have warm and cool tones
  Measured in kelvin which is a unit of temperature

## Slide 11: Reflectors
Light reflects in the equal but opposite direction when on a flat surface

## Slide 12: Reflectors continued
For a long time, reflector technology is what advanced the output of theatrical lighting fixtures
Made of metal or glass due to heat resistance
  Spherical reflector
  Parabolic reflector
  Ellipsoidal reflector
  Combination reflectors

## Slide 13: Spotlight vs Wash light
Spotlights (also called profile lights)
  Often smaller coverage of stage per instrument
  Usually has a sharper focus (hard edges)
  often uses less bold colors or N/C
Wash lights
  Wider coverage per instrument
  Soft edges that overlap other lights of same purpose
  Often used for general illumination (in a theater setting)

## Slide 14: Lighting Instruments

## Slide 15: Concept: Field angle vs Beam angle
Beam angle
Area of light that diminished by up to 50% from brightest point
Can appear to be a hotspot
  Less even field of light
Field angle
Area of light that diminished by up to 90% from brightest point
This is most of the lighting cone
  This excludes spill
Beam angle is always smaller or equal to field angle

## Slide 17: Ellipsoidal Reflector Spotlight (ERS)
Narrow cone of light
Usually a hard(er) edged light
Controllable shape via shutters
Adjustable focus via lens system
  Very concentrated with little spill
Measured in Field angle degrees
  Common 19°, 26°, 36° and 50°
Ellipse shaped reflector

## Slide 18: Beam/Field angles for ETC Source Four ERS
Degree Beam angle Field angle ~Max effective range
5° 6 ° 7 ° 160’
10° 8 ° 11 ° 125’
19° 15 ° 18 ° 70’
26° 18 ° 25 ° 59’
36° 27 ° 36 ° 47’
50° 36 ° 50 ° 31’
70° 60 ° 70 ° 22’
90° 79 ° 87 ° 15’

## Slide 19: Concept: flat and peak field of light
Flat
Peak

## Slide 20: Fresnel light
Ability to adjust hard and soft edge of light
  lamp and reflector slide relative to lens
  Done by a crank on back of fixture
  Further away, narrower beam
Spherical shaped reflector

## Slide 21: Fresnel spot and flood
Spot
Flood (may be a bit larger is size at same distance)

## Slide 22: Par can
Minimal adjustment
  rotation
Beam angle adjusted by swapping lamps

## Slide 23: Strip lights
Unique shape - wide and shallow
Multi circuit
  Often 3 or 4 circuits per unit
    Used for color mixing
Good for uplighting cyc
  Called a ground row
Also can be an effect light

## Slide 24: Cyc lights
Unique reflector shape "J”
  Shapes light to maximize vertical beam
Powerful lamps
  Usually 1,000 watts each
3 and 4 circuit units available
  1x4 and 2x2

## Slide 25: Cyc and ground row combined

## Slide 26: Follow Spotlights
Manually operated lights
  Mounted on a gimbal
  Balanced to move freely
Features
  Manual shutter
  Iris
  Focus
  Color/diffusion
Often use an arc lamp – no fade

## Slide 27: Booms and Ladders
Boom (aka Tree)
Ladder

## Slide 28: Lighting accessories
The following will be a list of more common accessories used in theater

## Slide 29: Gel and gobo’s
Gel and diffusion
Gobo (short for go between)

## Slide 30: Iris and Hats/snoots
Iris
Hat

## Slide 31: Doors and scrollers
Barn doors
Color scroller

## Slide 32: Rotators and Mirrors (intelligent)
Gobo rotator
Moving mirror