## Slide 1: Introduction to Stage Lights
Module 3 – Cables and connectors

## Slide 2: Types of conductors
Solid
Stranded

## Slide 3: Solid wire
Single wire core
  Jacketed
  Used for permanent installation

## Slide 4: Stranded wire
Multi-strand core
  Jacketed
  Used in both permanent and temporary installations
The more strands and thinner each strand, the more flexible the cable is

## Slide 5: Wire gauge
Gauge abbreviated as AWG (American Wire Gauge)
As the cross section of a conductor gets larger, the gauge number gets smaller
  Ex. a 12awg wire’s conductor is thicker than a 18awg
More than one conductor can be in a wire
  Denoted as 12/3 or 16/2 (gauge size conductor / number or conductors)
Individual conductors need to be insulated from each other
  Use plastic or rubber typically with an outer jacket to encase them all

## Slide 7: Color conventions in power cable
Hot – Black
Neutral – White
Ground – Green
“Black to brass, White to bright, green to ground”
Never assume homemade cables follow this and correct when possible

## Slide 8: Twistlock connector
3 conductor
  Locks in place using a small twist once pushed all the way in

## Slide 9: Stage pin connector
3 conductor
  No locking function
    Has to be taped
    Lose connections require a pin splitter
Green center, closer pin to center is white, black is further
Also caller 2-pin and ground (2P&G)

## Slide 10: Edison connector
3 conductor
  No locking function
  Used on consumer devices

## Slide 11: PowerCon connector
3 conductor
  Locking function
    Push in all the way and twist
      A button prevents untwisting

## Slide 12: True1 (TrueOne)
3 conductor
  Locking function
    Push in all the way and twist
      A button prevents untwisting

## Slide 13: 2fer (with stage pin connectors)
A “Y” adapter to provide power to 2 conventional fixtures
  Both fixtures will operate together
    No independent control
Yes, 3fers exist, but uncommon
  Due to ease of overloading

## Slide 14: Multi-cable (Socapex)
Comes is various lengths
  6 circuits worth
  Locking function by screw collar

## Slide 15: Fan in’s and fan outs
A way to break out individual circuits in multicable
  May have any type of connector on ends and don’t have to be the same

## Slide 16: Floor pockets, wall pockets, and raceways
Different locations to find circuits in theaters
Floor pockets are in the floor typically underneath a false door
Wall pockets are more exposed
Raceways are attached to battens