## Slide 1: Introduction to Stage Lights
Module 5 – Practicles and effects

## Slide 2: What is a practical?
Any working light source on stage
  Floor lamps
  Chandeliers
  Wall sconces
  Torches
In every case the appearance of the practical is relevant to the play
  Why, because these objects are seen
    Unlike stage lighting which is often hidden or masked

## Slide 3: Handheld lighting instruments
Aren’t objects an actor holds considered a prop – Yes
Depending on the structure of an organization
  The Props dept will take care of it
  The props dept will design and build the object, Lighting must electrify it
  The lighting dept will build and electrify it from designer’s reference image

## Slide 4: Purpose of practicals
Designed to look intentional and enhance the scene
Not look fake, cheesy, or distract
Not intended to illuminate the stage
  We have stage lighting for that
    DO want to give the illusion that they are the scenes light source
      Regularly use lower wattage lamps or run them less than full

## Slide 5: Fire
We do everything we can to prevent fire on stage
  This is why we fireproof curtains and treat scenery with fire retardant
    This is also why you see all raw wood painted over on Broadway touring sets
In many theaters it is 100% not allowed, nonnegotiable
In other theaters certain flame elements are allowed
  This is determined by fire code and the fire marshal
    If fire is going to be used, there is a stagehand in the wing holding an extinguisher

## Slide 6: Faking fire
If I can’t have fire, what am I to do?
Fire effects come in different shapes and sizes
  Depending on the need of your production, a safe alternative WILL exist

## Slide 7: How do you fake fire
In the case of a candle, battery operated options are available
  Available in tea light, stick and piler formats
  Most have a believable color and flicker effect
    Some even respond to movement and wind
What if it doesn’t fit inside my object?
  Not uncommon to disassemble to fit inside props

## Slide 8: How do you fake fire continued
What if I am trying to make a gas lamp?
  Often easier if fixed on stage
    Can be corded – no batteries
      Used to have to build a flicker circuit
      Now we have fire effect lights
    Use distress and wear to your advantage
      Soot and dirtied panes obscure view

## Slide 9: How do you fake fire continued
What about a fireplace
  Those exist too, with or without sound
  Fire inserts are incredibly believable
  Sometimes you can even hide a tv with a fire video playing for maximum realization

## Slide 10: How do you fake fire continued
What if I need a lot of fire?
  Iridescent silk,, fan and orange light
Best example I’ve seen is Pirates of Caribbean ride

## Slide 11: Other effect lights
Moon box
  Thin box using indirect light
    Hung behind scrim or cyc

## Slide 12: Stars
Often made from curtains and fiberoptic filaments
  These can also be rented

## Slide 13: Water
Caustics or ripples
  Originally made with a cookie sheet, mirror, fan and light
  Can also be made with gobo rotators

## Slide 14: Fog and haze effects
These regularly fall into lighting
  Haze is light particles floating in air
  Fog has 2 varieties
    Burst like smoke
    Low lying fog
      Some devices have built in lights