## Slide 1: Introduction to Stage Lights
Module 6 – Color theory

## Slide 2: Hue
Hue is the name of the color
  Red
  Orange
  Yellow
  Green
  Blue
  Violet

## Slide 3: Saturation
Saturation is how strong of a color is presented

## Slide 4: Value
Value is the brightness or darkness of a color
  This term is relative and used to compare different colors
  The brighter the color, the higher the value

## Slide 5: Tint
Tint is a color created from adding white to a hue

## Slide 6: Shade
Shade is adding black to a hue

## Slide 7: Tone
Tone is created by mixing a hue with grey

## Slide 8: Warm and cool colors

## Slide 9: How we “see” color
Every color we see is reflected
  The color we see is what’s not absorbed, what’s reflected

## Slide 10: Color Light Pigment

## Slide 11: Additive vs subtractive
Additive color (light)
  When more colors are added the new color gets closer to white
  Black is the absence of color
Subtractive color (pigment)
  When more colors are added the new color gets closer to black
  White is the absence of color

## Slide 12: Subtractive color in light

## Slide 13: What is a full spectrum light
Full spectrum means all colors of light are leaving the fixture
  If all colors are represented, the color of light would appear white
  LED fixtures have different colored diodes inside in order to represent the majority of the spectrum
  This is why white LED house lights are bad for growing plants
We can subtract color in light by using gel filters
  Gel prevents certain colors from passing through, changing the appearance of light

## Slide 14: Color of set and costume influence the color choices of the lighting designer

## Slide 15: Light positions
In theater we hang lights at various positions in order to not only light the scene but to create mood and to simulate time of day

## Slide 16: Front light
Front light easily illuminates, and doesn’t create much shadow on figure (exception under chin)
Rather flattening, features don’t “pop”

## Slide 17: Angled front light
Illuminates the majority of the figure, cleans up some shadow under chin, leaves 1/3 of face dark
Features begin to stand out
Has a “dramatic feel”
SR Front 

## Slide 18: Side light
Used to make features most defined
½ face in shadow
When paired with a complimenting light on opposite side, created small shadow line down middle of face
Very useful for dance

## Slide 19: Top light
Used to glow crown of head and shoulders
When used with a saturated hue of light, creates an interesting effect

## Slide 20: Front Uplight
More of an effect light
Eliminates under chin shadow
  Also lights under wide rimmed hats
Reminiscent of foot lights from old theaters
Also the “scary ghost story” look

## Slide 21: Silhouette
Another effect lighting position
Created by only using cyc lights
  Frequently used in dace

## Slide 22: A lighting key explained
A lighting key is a pictorial reference of fixtures for any one common area on the stage
Consists of all fixtures with angles and gel colors (and gobos) defined
One of the pieces of paperwork generated by a lighting designer

## Slide 23: Complimentary color concept
Complimentary colors are a primary and the opposite secondary color on the color wheel
When complimentary colors are mixed, in light we see white light
  We also see colored shadows

## Slide 24: Colored shadows
What direction are the red and blue light coming from?

## Slide 26: Bold color directional light for effect